## Slide 1: WF on timing relationship for V2V sensing and resource selection
Intel
3GPP TSG RAN WG1 Meeting #86 R1-168382
Gothenburg, Sweden, 22nd - 26th August 2016
Agenda item - 7.2.2.2.2

## Slide 2: Background
The timing relationship between sensing window, reselection trigger, transmission instance of control and data were discussed at the RAN1#84bis
The following notations were introduced (see next slide)
  n – time instance of the resource reselection trigger;
  [n-a; n-b] – sensing window associated with trigger at time instance n;
  (n+c) – time instance of SCI transmission for triggered resource (re)-selection;
  (n+d) – time instance of the first TB transmission after resource reselection;
  (n+e) – time instance(s) of subsequent TB(s) transmission e = [e1, e2, e3,…]

## Slide 3: Timing Relationship
At the RAN1#84bis the timing relationship between sensing window and transmission of control/data is defined with respect to reselection trigger

## Slide 4: Potential Problem
Time instances of reselection trigger and packet arrival events can be different
The timing relationship between sensing window and control/data transmission should be defined with respect to the time instance of packet arrival to low layer buffers(packet generation time) instead of time instance of reselection trigger
The timing relationship between sensing windows and transmission instance of data/control needs to be defined

## Slide 5: Proposal
Redefine ‘n’ as a time instance of the arrival to PDCP layer of the first packet after resource (re)-selection is triggered
Time to make a resource reselection decision after initiation of resource (re)-selection is fixed

## Slide 6: Example
Example of proposed timing relationship