## Slide 1: WF on evaluation assumptions related to outdoor micro cell TRP
3GPP TSG RAN WG1 Meeting #86 R1-168387
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda Item: 8.1.7
ZTE Corporation, ZTE Microelectronics, InteI Corporation

## Slide 2: Background
The possible options for outdoor micro cell TRP antenna element model and placement:
  Option 1: Omni in horizontal, directional in vertical ([5]dBi gain, HPBW [400], vertical tilt 900)
    Dropping in the center of the hotspot area
  Option 2: Directional in horizontal, directional in vertical ({8dBi gain, HPBW = 650}; {4dBi gain, HPBW = 1300})
    One-sector deployment
      Dropping of TRP and TRP antenna orientation according to TR 36.897 (non co-channel hetnet deployment)
    Three-sector deployment
      Dropping of TRP in the center of the hotspot area
      Option A: Azimuth orientation of TRP antenna is random
      Option B: Azimuth orientation of TRP is according to macro TRP deployment
  RAN1 to choose from the above options in RAN1#86 for the above 6GHz and below 6GHz and other options are not precluded

## Slide 3: Proposal 1
  Adopt Option 1 and Option 2 with one sector deployment for micro cell TRP deployment in dense urban scenario, i.e.
    Option 1: Omni in horizontal, directional in vertical (5dBi gain, HPBW 400, vertical tilt 900, Am=20dB, SLAv=30dB)
      Dropping in the center of the hotspot area
    Option 2: Directional in horizontal, directional in vertical (8dBi gain, HPBW = 650, vertical tilt 900 , Am=30dB, SLAv=30dB )
    One-sector deployment
      Dropping of TRP and TRP antenna orientation according to TR 36.897 (non co-channel hetnet deployment)
  The maximum distance (din + dout) from a UE to a closest TRP shall not exceed R (UE dropping radius).

## Slide 4: Proposal 2
Number of the micro TRPs per macro TRP | Minimum distance between Micro TRP centers (m) | Radius of UE dropping within a cluster: R (m)
3 | 40 | <40
6 | 32 | <40
9 | 25 | <40
  Reduce the minimum distance between micro TRPs and radius of UE dropping to the values in the following table:
  Adopt the following minimum distances:
Parameters | Value
The minimum distance between Macro TRP and UE | 10m
The minimum distance between Micro TRP and UE | 10m