## Slide 1: WF on number of HARQ processes for NR
Qualcomm, DCM, ZTE, Verizon, [CMCC]
3GPP TSG RAN WG1 #86 R1-168430
Gothenburg, Sweden, Aug 22 - 26, 2016
Agenda item: 8.1.3

## Slide 2: Observations
The support of self-contained single interlace operation is useful for the following use cases:
  Ultra reliability low latency communication
  Forward compatibility
  Low complexity high throughput support
  Dynamic TDD
  NR over unlicensed band
  …

## Slide 3: Way Forward
Scheduling Unit (SU) terminology: TBD
NR should target to support at least the following for some UEs and base stations:
  Self-contained 1 HARQ process:
    A UE can be configured with back-to-back single HARQ process:
      Ctrl in SU(N); Data in SU(N); ACK in SU(N) for DL; earliest reTx in SU = (N+1)
  More than 1 HARQ processes:
    For example: 2 HARQ processes
      Option 1: Ctrl in SU(N); Data in SU(N); ACK in SU(N) for DL; earliest reTx in = SU(N+2)
      Option 2: Ctrl in SU(N); Data in SU(N); ACK in SU(N+1) for DL; earliest reTx in = SU(N+2)
    FFS: other number of HARQ processes
  Other proposals are not preclude