## Slide 1: Way forward on the waveform for above 40GHz
Nokia, ASB, Intel, InterDigital, Mitsubishi Electric, Qualcomm, MediaTeK, Ericsson, NTU, National Instruments
3GPP TSG RAN WG1 Meeting #86 R1-168525
Gothenburg, Sweden, 22 – 26 Aug 2016
Agenda Item: 8.1.2.1

## Slide 2: Background
The current RAN1 agreement on Waveform only covers below 40GHz
  At least up to 40 GHz for eMBB and URLLC services, NR supports CP-OFDM based waveform with Y greater than that of LTE (assuming Y=90% for LTE) for DL and UL, possibly with additional low PAPR/CM technique(s) (e.g., DFT-S-OFDM, etc.)
  WRC-15 results includes much wider spectrum above 40GHz (e.g. 66-76GHz, 81-86 GHz)
45.5-47GHz
(2.5GHz)
47-50.2 GHz
(3.2GHz)
7.9GHz
50.4-52.6 GHz
(2.2GHz)
66-76 GHz
(10 GHz)
81-86 GHz
(5 GHz)

## Slide 3: Background
Especially for higher band (e.g. 66-76GHz, 81-86GHz), single-carrier waveforms are proposed in order to overcome the limitations about the band (e.g. noise limited, poor PA efficiency, higher PN noise and Doppler effect etc).
Most waveform proposals specified for on above 40GHz below are single-carrier based.
  GI-DFT-s-OFDM (R1-167126)
  UW-DFT-s-OFDM (R1-166227, R1-167558)
  BWSC (R1-167125)
  Null CP-SC (R1-167794)
  CPS-OFDM (R1-167820)

## Slide 4: Proposal
When considering DL and UL waveforms for spectrum band above 40GHz, RAN1 should also consider the waveform property in terms of providing high robustness to
  Low PA efficiency
  Phase Noise and Doppler impairments