## Slide 1: WF on the unified structure of DL sync signal
Intel Corporation, NTT DOCOMO, ZTE, ZTE Microelectronics, ETRI, InterDigital
3GPP TSG RAN WG1 Meeting #86b
Lisbon, Portugal 10th – 14th October 2016
Agenda item: 8.1.5.1
R1-1610522

## Slide 2: Background
In RAN1#86, the following was agreed in relevance to NR DL synchronization:
  RAN1 should strive for a common framework, including for example structure of synchronization signals, for initial access
This WF proposes the unified structure for DL sync signal transmission to cover various scenarios (according to different frequency ranges, single/multi-beam operations) and use cases (eMBB, URLLC)
In some scenarios, e.g., unlicensed operation, overhead reduction, it is useful to occasionally turn off SS transmission

## Slide 3: Proposals
PSS, SSS and/or PBCH can be transmitted within a ‘SS block’
  FFS: details how to compose PSS, SSS and/or PBCH
One or multiple ‘SS block(s)’ compose an ‘SS burst’
  FFS: Number of ‘SS block(s)’ (defined as duration of ‘SS burst’)
  FFS: whether or not ‘SS block(s)’ are consecutive
One or multiple ‘SS burst(s)’ compose an ‘SS burst series’
  FFS: Periodicity and number of ‘SS burst’
  FFS: Transmission instances of ‘SS burst series’

## Slide 4: Examples (BF & non-BF)
1) Omni-Tx – e.g. <6GHz
2) Quasi-Omni-Tx – e.g. >6GHz: Same beam within SS burst, different beams between SS bursts, Regular beam pattern between SS bursts series
3) Directional-Tx – e.g. >6GHz: different (narrow/wide) beams between SS within SS burst, different beams between SS bursts, Regular beam pattern between SS bursts series