## Slide 1: Way forward on NR HARQ For: Decision AI: 8.1.7.2
Intel, Nokia, ASB, AT&T, OPPO, MediaTek
3GPP TSG-RAN WG1 #86bis R1-1610631
Lisbon, Portugal 10th - 14th October 2016

## Slide 2: Background
Agreements from RAN1 #86:
The following is supported for NR
  From UE perspective, HARQ ACK/NACK feedback for multiple DL transmissions in time can be transmitted in one UL data/control region is supported
  Some or all of the following timing relationships can be indicated to a UE dynamically by the L1 DL signaling (FFS: explicit or implicit)
    Timing relationship between DL data reception and corresponding acknowledgement
    Timing relationship between UL assignment and corresponding UL data transmission
    Note: Default value, if any, for each timing relationship is FFS (agreement from RAN1 #85)
    Note: Potential values for each timing relationship has to be studied further considering e.g., UE processing capability, gap overhead, UL coverage, and etc. (agreement from RAN1 #85)
    Note: Other means of indicating the timing relationship are not precluded
  Some or all of the following timing relationships can be indicated to a UE semi-statically (FFS: explicit or implicit)
    Timing relationship between DL data reception and corresponding acknowledgement
    Timing relationship between UL assignment and corresponding UL data transmission
    Note: Default value, if any, for each timing relationship is FFS (agreement from RAN1 #85)
    Note: Potential values for each timing relationship has to be studied further considering e.g., UE processing capability, gap overhead, UL coverage, and etc. (agreement from RAN1 #85)
    Note: Other means of indicating the timing relationship are not precluded

## Slide 3: Proposal 1
Timing relationship between DL data reception and corresponding acknowledgement can be dynamically indicated in the DCI
  FFS: minimum interval
Timing relationship between UL assignment and corresponding UL data transmission can be dynamically indicated in the DCI
  FFS: minimum interval

## Slide 4: Proposal 2
Timing relationship between DL data reception and corresponding acknowledgement can be semi-statically indicated to a UE via higher layer signaling.
  FFS: minimum interval
Timing relationship between UL assignment and corresponding UL data transmission can be semi-statically indicated to a UE via higher layer signaling.
  FFS: minimum interval

## Slide 5: Proposal 3
Support at least multiple DL HARQ processes to support consecutive DL transmissions for eMBB.
Support at least multiple UL HARQ processes to support consecutive UL transmissions for eMBB.