## Slide 1: WF on TR Structure for NR Multiple Access
Nokia, ASB
3GPP TSG RAN WG1 #86bis R1-1610686
Lisbon, Portugal
10th – 14th October 2016
Agenda item: 8.1.1.2
Document for decision

## Slide 2: Back ground (1/7)
Agreements
  In RAN1#84bis
    Non-orthogonal multiple access should be investigated for diversified NR usage scenarios and use cases
    At least for UL mMTC, autonomous/grant-free/contention based non-orthogonal multiple access should be studied
  In RAN1#85
    Autonomous/grant-free/contention based UL non-orthogonal multiple access has the following characteristics
      A transmission from UE does not need the dynamic and explicit scheduling grant from TRP
      Multiple UEs can share the same time and frequency resources
      To be continued

## Slide 3: Back ground (2/7)
    (continued)
    For autonomous/grant-free/contention based UL non-orthogonal multiple access, the following should be studied
      Collision of time/frequency resources from different UEs, solutions potentially including
        E.g., code, sequence, interleaver pattern
      UL synchronization (DL synchronization assumed)
        Case 1: Timing offsets between UEs are within a cyclic prefix
        Case 2: Timing offsets between UEs can be greater than a cyclic prefix, FFS the exact model of timing offsets
      Requirement for power control
        Case 1: Perfect open-loop power control, i.e., equal average SNR between UEs for potentially link level calibration
        Case 2: Realistic open-loop power control with certain alpha and P0 values
        Case 3: Close-loop power control
      Receiver impact

## Slide 4: Back ground (3/7)
    (continued)
    NR supports at least synchronous/scheduling-based orthogonal multiple access for DL/UL transmission schemes, at least targeting for eMBB
      Note: Synchronous means that timing offset between UEs is within cyclic prefix by e.g. timing alignment

## Slide 5: Back ground (4/7)
    (continued)
    NR supports at least synchronous/scheduling-based orthogonal multiple access for DL/UL transmission schemes, at least targeting for eMBB
      Note: Synchronous means that timing offset between UEs is within cyclic prefix by e.g. timing alignment
  In RAN1#86
    NR should target to support UL “autonomous/grant-free/contention based” at least for mMTC
    At least the following options for “autonomous/grant-free/contention based” UL transmission should be studied
      Opt. 1: a UE performs random resource selection
        Details FFS
      Opt. 2: a UE’s resource is pre-configured by eNB or pre-determined
        Details FFS
      Other options are not precluded
    To be continued

## Slide 6: Back ground (5/7)
    A MA physical resource for “grant-free” UL transmission is comprised of a time-frequency block
      Note: spatial dimension is not considered as a physical resource in this context
    A MA resource is comprised of a MA physical resource and a MA signature, where a MA signature includes at least one of the following:
      Codebook/Codeword
      Sequence
      Interleaver and/or mapping pattern
      Demodulation reference signal
      Preamble
      Spatial-dimension
      Power-dimension
      Others are not precluded
    To be continued

## Slide 7: Back ground (6/7)
    continued
    Details on MA physical resource and MA signature resource FFS
    Continue study at least the following:
      Handling of potential collisions of MA signatures
      Retransmission/repetition and potential combining, e.g. HARQ
      Potential link adaptation, e.g. MCS/signature re-assigning
      Relationship between grant-free and grant-based transmissions and associated UE behavior
    Advanced receiver capabilities including complexity analysis

## Slide 8: Back ground (7/7)
Observation
  The following non-orthogonal multiple access schemes have been reported up to RAN1#86 for at least UL NR MA (listed in the order of proposed time, i.e., increasing tdoc number)
    Sparse code multiple access (SCMA) (e.g., R1-162153)
    Multi-user shared access (MUSA) (e.g., R1-162226)
    Low code rate spreading (e.g., R1-162385)
    Frequency domain spreading (e.g., R1-162385)
    Non-orthogonal coded multiple access (NCMA) (e.g., R1-162517)
    Non-orthogonal multiple access (NOMA) (e.g., R1-163111)
    Pattern division multiple access (PDMA) (e.g., R1-163383)
    Resource spread multiple access (RSMA) (e.g., R1-163510)
    Interleave-Grid Multiple Access (IGMA), (e.g., R1-163992)
    Low density spreading with signature vector extension (LDS-SVE) (e.g., R1-164329)
    Low code rate and signature based shared access (LSSA), (e.g., R1-164869)
    Non-orthogonal coded access (NOCA), (e.g., R1-165019)
    Interleave Division Multiple Access (IDMA), (e.g., R1-165021)
    Repetition division multiple access (RDMA), (e.g., R1-167535)
    Group Orthogonal Coded Access (GOCA), (e.g., R1-167535)

## Slide 9
In order to proceed with the multiple access discussion, we define the sections to be included in the TR 38.802
NOMA discussion and grant-free discussion will be described separately
For NOMA, general framework, BS receiver schemes and evaluation results will be captured
All the grant-free features agreed to be studied will be included in TR document
Proposals (1/2)

## Slide 10
Companies agree to include following sections in TR 802 for MA
8.1.3 Multiple access scheme
  8.1.3.1 General framework of UL multiple access schemes
  8.1.3.2 UL grant-free
    8.1.3.2.1 Definition and usecase of UL grant-free access
      8.1.3.2.1.1 Definition
      8.1.3.3.1.2 Use cases
    8.1.3.2.2 Access mode switching
    8.1.3.2.3 Physical resource and signatures
    8.1.3.2.4 Procedure design and channel formats
      8.1.3.2.4.1 Procedure options and channel formats
      8.1.3.2.4.2 Retransmission schemes
      8.1.3.2.4.3 Link adaptation
  8.1.3.3 Initial observations
    8.1.3.3.1 Candidate BS receiver schemes and PHY abstraction
    8.1.3.3.2 UL Link-level performance evaluation
    8.1.3.3.3 UL System-level performance evaluation
  8.1.3.4 Potential UL specification impacts
Proposals (2/2)