## Slide 1: WF on PRS-Based RSRP/RSRQ Measurement and Reporting for PRS-Based Beacon
Nokia, Alcatel-Lucent Shanghai Bell
R1-1610928
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal, October 10-14, 2016
Agenda item 7.2.6.2

## Slide 2: Background
In RAN1#86 meeting, it has been agreed that
  Additional PRS configurations for PRS-based TBS
  PRS-only TBS Transmission Points (TPs):
    For the purpose of RSTD measurements from a PRS-only TBS TP, a UE shall not assume any other signals or physical channels are present other than PRS.
    Add an indicator in the OTDOA assistance data which indicates that assistance is provided for a PRS-only TBS TP.
RSRP/RSRQ are the important parameters for positioning purpose, for example E-CID positioning as well as TP selection for OTDOA positioning. So it would be valuable to support RSRP/RSRQ reporting for PRS-based beacon. However RSRP/RSRQ are measured by CRS or CSI-RS downlink reference signals in the existing LTE network, but PRS-based beacon is only used for PRS transmission in order to reduce the beacon deployment cost. Therefore it is proposed to reuse PRS for RSRP/RSRQ measurement of the PRS-based beacon.

## Slide 3: Proposals
Support PRS-based RSRP/RSRQ measurement and reporting
  Interface/protocol
    Alt. 1: PRS-based RSRP/RSRQ measurement configuration and reporting by RRC signalling
    Alt. 2: PRS-based RSRP/RSRQ measurement configuration and reporting by LPP
  Number of PRS-based beacons for RSRP/RSRQ measurement and reporting
    Up to 9 PRS-based beacons per UE for RSRP/RSRQ
  Value range
    The value range of PRS-based RSRP: INTEGER (0…97) [Same as RSRP value range in LPP]
    The value range of PRS-based RSRQ: INTEGER (0…34) [Same as RSRQ value range in LPP]
  Reporting Mode
    Alt. 1: Periodic: 120ms, 240ms, 480ms, 640ms, 1024ms, 2048ms, 5120ms, 10240ms, 1min, 6min, 12min, 30min, 60min [Same as E-CID measurement periodicity in LPP]
    Alt. 2: Aperiodic
    Alt. 3: Event triggered, for example PRS resource becomes better than absolute threshold