## Slide 1: WF on NR channel coding selection
CMCC, CATR, OPPO, InterDigital,, AccelerComm,, MediaTek, ZTE, ZTE Microelectronics
R1-1610982
3GPP TSG RAN1 #86bis
Lisbon, Portugal, Oct. 10 – 14, 2016
Agenda Item: 8.1.3.1

## Slide 2: Proposal
For eMBB DL data
  LDPC is selected as the channel coding scheme for TBS at least larger than X bits
  Turbo is selected as the channel coding scheme for TBS smaller than X bits
For eMBB UL data
  LDPC is selected as the channel coding scheme for TBS at least larger than Y bits
  Polar is selected as the channel coding scheme for TBS smaller than Y bits
For DL control, polar is selected as the channel coding scheme