## Slide 1: WF on Observations of Packet Size Distribution for eMBB Data
Ericsson, Nokia, ASB, Qualcomm, Samsung, Intel
R1-1613095
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th - 18th November 2016
Agenda item 7.1.5.1

## Slide 2: Background
Agreement in RAN1#86bis
  The channel coding scheme for eMBB data is LDPC, at least for information block size > X
  FFS until RAN1#87 one of Polar, LDPC, Turbo is supported for information block size of eMBB data <= X
    The selection will focus on all categories of observation, including overall implementation complexity, regardless of the number of coding schemes in the resulting solution (except if other factors are generally roughly equal)
  The value of X is FFS until RAN1#87, 128 <= X <= 1024 bits, taking complexity into account
  The channel coding scheme(s) for URLLC, mMTC and control channels are FFS

## Slide 3: Proposal: Observation on Packet Sizes
Reference: R1-1611710
Data volume
  In a typical LTE network, only 3.4% of the DL data volume is carried by IP packets with size 1000 bytes or less
  In a typical LTE network, 25% of the UL data volume is carried by IP packets with size 52 bytes or less
    Due to IP packet size of 40 bytes and 52 bytes
Packet frequency
  Only 0.02% of DL IP packets are smaller than 40 bytes, which corresponds to transport block size of 376 bits
  ~10% DL IP packets are 52 bytes or less
    Due to IP packet size of 40 bytes and 52 bytes
  Only 0.08% of UL IP packets are smaller than 40 bytes, which corresponds to transport block size of 376 bits
  ~75% UL IP packets are 52 bytes or less
    Due to IP packet size of 40 bytes and 52 bytes

## Slide 4: Proposal: Observation on Packet Sizes (Cont.)
40 bytes at IP layer correspond to K=400 bits at the input to the channel encoder:
  K=400 bits is arrived at: 400 bit = (40 byte+7 byte)*8 + 24 bit
    7 byte is the minimum header size from PDCP+RLC+MAC layers
    24 bit for TB-level CRC
To arrive from an IP packet to an information block for channel encoder, other procedures like concatenation and segmentation are applied
  For LTE, when code block segmentation is applied, the minimum K is: K=6144/2 = 3072 bits

## Slide 5: Proposal
Coding schemes for downlink eMBB data should be optimized for large transport block sizes
For both DL and UL, coding schemes for eMBB data should be selected based on the performance for info block sizes K>=400 bits
  TBS design should cover the full range of info block size that NR needs
  It is not to be assumed that eMBB channel coding scheme is designed to cover K>=400 bits only

## Slide 6: Backup