## Slide 1: WF on DCI design for multicast in FeMTC
ZTE, Nokia, ASB, Ericsson …
R1-1613131
3GPP TSG RAN WG1 Meeting #87
Reno, USA, November 14-18, 2016
Agenda item 6.2.8.2

## Slide 2: Background
In RAN1#86bis meeting, regarding FeMTC Multicast, the followings are agreed:
Max channel bandwidth and max TBS for SC-MTCH PDSCH transmission to BL/CE UEs:
  Option 1: According to Rel-13 Cat-M1 limitations (i.e. 6 PRBs and 1000 bits)
  Option 2: Configurable per SC-MTCH (with minimum maximum values of 6 PRBs and 1000 bits)
Max channel bandwidth and max TBS for SC-MCCH PDSCH transmission to BL/CE UEs:
  Option A: According to Rel-13 Cat-M1 limitations (i.e. 6 PRBs and 1000 bits)
  Option B: Configurable per SC-MCCH (with minimum maximum values of 6 PRBs and 1000 bits)
From physical layer point of view,
  All four options are feasible.
  Option 2 may have performance benefits over Option 1.
The maximum number of on-going SC-MTCHs supported by SC-MCCH is reduced compared to LTE.
Send LS to RAN2 to
  Inform RAN2 that RAN1 assumes the maximum number of on-going SC-MTCHs supported by SC-MCCH is reduced compared to LTE
  Request RAN2 to inform RAN1 of the maximum number of on-going SC-MTCHs supported by SC-MCCH in FeMTC.
  Request RAN2 to inform RAN1 whether and how segmentation of SC-MCCH will be supported in Rel-14.
For the search space scheduling SC-MCCH
  UE monitoring of blind decoding candidates is based on FFS: Type1-CSS or Type2-CSS for MPDCCH
  Rmax, and G values are configured per SC-MCCH by higher layers
    FFS the configuration of other parameters, e.g., narrowband.
Frequency hopping is supported in multicast to BL/CE UEs at least for max PDSCH channel bandwidth of 6 PRBs.
  FFS whether the frequency hopping is controlled by the same SIB parameters as other DL transmissions or by separate SIB parameters and/or DCI

## Slide 3: Background
In RAN2#95bis meeting, regarding Multicast, the followings are agreed:
  We consider to make the following agreement (working assumption for now):
    MT (paging) vs. SC-PTM: MT (Paging) has higher priority than SC-PTM
    MO (except signalling) vs SC-PTM: UE implementation
    MO signalling vs SC-PTM: MO signalling has priority.

## Slide 4: Proposal
DCIs for scheduling SC-MCCH is based on DCI format 6-2 with at least the following fields:
  Resource assignment
  Number of PDSCH repetitions
  MCS
  Number of MPDCCH repetitions
  FFS: Frequency-hopping flag
DCIs for scheduling SC-MTCH include at least the following fields:
  Frequency-hopping flag
  Resource assignment
  Number of PDSCH repetitions
  MCS
  Number of MPDCCH repetitions
The sizes of the DCI fields are FFS.
  To accommodate Rel-14 enhancement of max TBS and max channel bandwidth.
Other DCI fields than the ones listed above are not precluded.