## Slide 1
3GPP TSG RAN WG1 Meeting #87 R1-1613159 Reno, 14th - 18th Nov 2016
Agenda item: 7.1.3.1
WF on DL MIMO transmission schemes for data transmission
Huawei, HiSilicon, Nokia, ASB, NTT DOCOMO, Ericsson, MTK

## Slide 2: Background
Support downlink transmission scheme(s) achieving diversity gain at least for some control information transmission
  Exact scheme is for further study.
  Specification support for such transmission schemes, i.e., the scheme(s) may or may not be implemented in spec-transparent manner
  Note: The data/control channel transmission is at least based on DM-RS for demodulation.
DL and UL transmission techniques should be studied to provide robustness against imperfect CSI and mobility
  e.g.) The techniques using a subset of beams/precoders may include beam cycling, beam broadening, etc.
  e.g.) In case of DL and FDD, this technical scope may include semi-open-loop MIMO technique being discussed in LTE eFD-MIMO.

## Slide 3: Proposal
Support at least the following DMRS based DL MIMO transmissions for data in NR,
  Scheme 1: transmission where data and DMRS are transmitted with the same precoding matrix
    Demodulation of data at the UE does not require knowledge of the precoding matrix used at the transmitter
    Note: spatial multiplexing and rank-1 are included
  Scheme 2: Transmit diversity
    Demodulation of data at the UE requires knowledge of the relation between DMRS ports and data layers
    SFBC is at least supported
  Scheme 3: Spatial multiplexing where data and DMRS are not restricted to be transmitted with the same precoding matrix
    Demodulation of data at the UE requires knowledge of the relation between DMRS ports and data layers
    E.g., Large delay CDD, Layer shifting
    Note: DMRS can be precoded or not precoded