## Slide 1: WF on frequency granularity for CSI reporting in NR
LG Electronics, NTT DOCOMO, Samsung, Intel, [Nokia], Ericsson, …
R1-1613176
3GPP TSG RAN1 #87
Reno, USA, Nov. 14 – 18, 2016
Agenda Item: 7.1.3.3.

## Slide 2: Background
In NR, different subcarrier spacings or scheduling time units can be multiplexed in different parts of system bandwidth for supporting different services such as eMBB, URLLC, mMTC.
The different parts would have different CSI properties such as interference condition, supportable MCS, etc.

## Slide 3: Proposal
For CSI reporting for a component carrier, at least three different frequency granularities should be considered in the study
  Wideband CSI
    Wideband size is determined by UE RF capability of receiving DL signal.
      Location of wideband could be configurable by network.
    Used for analog beam management at least.
  Partial band CSI
    Alt1. UE-specifically configurable bandwidth
    Alt2. The size is determined by the composition of numerologies or scheduling time units within the UE-specific wideband.
      Applicable only when different numerology or scheduling time unit are multiplexed within wideband.
    Used for managing CQI CSI per service at least
  Subband CSI
    The band size is determined by dividing wideband or partial band to multiple bands.
    Used for frequency selective scheduling and subband precoding at least

## Slide 4: Example