## Slide 1: WF on NR UE Requested Beam Switching
Intel Corporation, Samsung
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th –18th November 2016
Agenda: 7.1.3.3
R1-1613289

## Slide 2: Agreement from RAN1#86b
NR supports mechanism(s) in the case of link failure and/or blockage for NR
  Whether to use new procedure is FFS
Study at least the following aspects:
  Whether or not an DL or UL signal transmission for this mechanism is needed
    E.g., RACH preamble sequence, DL/UL reference signal, control channel, etc.
  If needed, resource allocation for this mechanisms
    E.g., RACH resource corresponding mechanism, etc.

## Slide 3: Agreement from RAN1#86b
Support at least network triggered aperiodic beam reporting:
  Aperiodic beam reporting is supported under P-1, P-2, and P-3 related operations
  FFS beam reporting details
  FFS: UE assisted/initiated aperiodic beam reporting
  FFS: In case of UE assisted/initiated aperiodic beam reporting, UE request message can be transmitted on a reserved/dedicated/common uplink channel (e.g. physical random access channel, physical uplink control channel).
Further study is needed whether semi-persistent/periodic/event-triggered beam (network triggered or UE assisted/initiated) reporting is needed

## Slide 4: Proposal
NR supports UE requested beam switching mechanism
  Study different beam measurement reports according to different measurement procedures P-1/P-2/P-3
  Study SR and PRACH as a candidate request channel