## Slide 1
WF on common control resource set
Qualcomm, ZTE,…
R1-1613314
3GPP TSG RAN WG1 #87
Reno, USA, 14th – 18th November 2016
Agenda item 7.1.4.1

## Slide 2: Background
RAN1#86bis agreements on RS for control
  Both UE/PDCCH-specific DMRS and Share/Common RS for PDCCH reception should be supported.
  A UE monitors for downlink control information in one or more “control sub-band”
RAN1 #86bis agreement on RS for tracking
  Reference signal for time/freq tracking:
    FFS on new RS or re-use RS for other functionalities
  Reference signal for RLM
    FFS on new RS or re-use RS for other functionalities
  Reference signal for RRM
    FFS on new RS or re-use RS for other functionalities

## Slide 3: Proposal
A common control resource set is define with parameters (location, bandwidth, numerology, number of OFDM symbols, etc) defined in MIB, if multiple sets of parameters are defined for one sync channel numerology
The common control resource set uses common/shared RS
  The common control resource set carries at least DL grants for initial access and MSIB
The eNB maintains the phase continuity of common/shared RS in common control resource set over time, at least when the common/shared RS in adjacent slots are targeting the same set of UEs.
FFS if the common control resource set always covers the sync channel in frequency domain