## Slide 1: WF on PDSCH/PUSCH channel bandwidth allocation for FeMTC UEs
Apple, Ericsson, Intel, XiaoMi, OPPO, Vivo, NEC, Sony, ZTE, LG Electronics, Qualcomm, Sierra Wireless
R1-1613339
3GPP TSG RAN WG1 Meeting #87
Reno, Nevada, USA, 14th – 18th Nov 2016
Agenda item 6.2.8.1.1

## Slide 2: Background
RAN1 has made the following agreements on larger max PDSCH/PUSCH channel bandwidth for Rel-14 BL UEs and non-BL UEs:
  For Rel-14 BL UEs in CE mode A and CE mode B, the single larger maximum UE channel BW for PDSCH in RRC connected mode is 5 MHz.
  For Rel-14 BL UEs in CE mode A, the single larger maximum UE channel BW for PUSCH in RRC connected mode is 5 MHz.
  For Rel-14 non-BL UEs in CE mode A and CE mode B, the larger maximum UE channel BW for PDSCH in RRC connected mode is 5 or 20 MHz.
  For Rel-14 non-BL UEs in CE mode A, the larger maximum UE channel BW for PUSCH in RRC connected mode is 5 or 20 MHz.
  Rel-14 non-BL UE may also support Rel-13 CE mode A and CE mode B .
  The wider bandwidth operation is enabled by eNB .

## Slide 3: Proposal
Proposal 1: Rel-14 BL/non-BL UE in CE Mode A support independent max PDSCH/PUSCH channel bandwidth configurations.
Proposal 2: Rel-14 BL /non-BL UE max PDSCH and PUSCH channel bandwidths are configured semi-statically through RRC signaling
  This does not have an impact on whether the Rel-14 DCI formats should be same size or not as Rel-13 DCI formats