## Slide 1: WF on max channel BW for non-BL UEs
Intel Corporation
R1-1613358
3GPP TSG RAN WG1 Meeting #87
Reno, Nevada, USA, 14th – 18th Nov 2016
Agenda item 6.2.8.1.2

## Slide 2: Background
Agreement from RAN1 #86bis meeting:
  Rel-14 non-BL UE can support CE mode A in connected mode with a maximum PDSCH/PUSCH channel bandwidth of either 5 or 20 MHz.
    Rel-14 capability signaling is introduced to differentiate non-BL UEs with respect to maximum UE channel BW support in CE.
  Rel-14 non-BL UE may also support Rel-13 CE mode A and CE mode B.
  A Rel-14 non-BL UE supporting CE mode A operation with 20-MHz maximum PDSCH/PUSCH channel bandwidth also supports CE mode A operation with 5-MHz maximum channel bandwidth.

## Slide 3: Proposals
The following RAN1 agreement is modified for max channel BW for PUSCH for non-BL UEs
  From
    Rel-14 non-BL UE can support CE mode A in connected mode with a maximum PDSCH/PUSCH channel bandwidth of either 5 or 20 MHz
  To
    Rel-14 non-BL UE can support CE mode A in connected mode with a maximum PDSCH channel bandwidth of either 5 or 20 MHz
    Rel-14 non-BL UE can support CE mode A in connected mode with a maximum PUSCH channel bandwidth of either 5 MHz
Rel-14 non-BL UEs can support CE mode B in connected mode with a maximum PDSCH channel bandwidth of either 5 or 20 MHz
Rel-14 non-BL UEs can support CE mode B in connected mode with a maximum PUSCH channel bandwidth of 1.4 MHz