## Slide 1
WF on RS for common control resource set
Qualcomm, ZTE
R1-1613399
3GPP TSG RAN WG1 #87
Reno, USA, 14th – 18th November 2016
Agenda item 7.1.3.2

## Slide 2: Background
RAN1#86bis agreements on RS for control
  Both UE/PDCCH-specific DMRS and Share/Common RS for PDCCH reception should be supported.
  A UE monitors for downlink control information in one or more “control sub-band”
RAN1 #86bis agreement on RS for tracking
  Reference signal for time/freq tracking:
    FFS on new RS or re-use RS for other functionalities
  Reference signal for RLM
    FFS on new RS or re-use RS for other functionalities
  Reference signal for RRM
    FFS on new RS or re-use RS for other functionalities

## Slide 3: Background
RAN1#87 agreements on control
  The time/freq. resource containing at least one search space is obtained from MIB/system information/implicitly derived from initial access information
  ….
  At least for single-stage DCI design:
  A control resource set (formerly called control subband) is, in the frequency domain, a set of PRBs within which the UE attempts to blindly decode downlink control information
    The PRBs may or may not be frequency contiguous
    A UE may have one or more control resource sets
    Working assumption: One DCI message is located within one control resource set

## Slide 4: Proposal
At least one control resource set uses common/shared RS
The common/shared RS in at least one control resource set is transmitted following a certain periodicity and pattern over time
  FFS: the periodicity and pattern