## Slide 1: WF on sPUCCH sTTI mapping
Ericsson, Nokia, Alcatel-Lucent Shanghai Bell, Samsung, LG Electronics
R1-1613414
3GPP TSG RAN1 #87
Reno, Nevada (US), Nov 14 - 18, 2016
Agenda item 6.2.10.2.3

## Slide 2: Background
The sTTI mapping of the sPUCCH is still not decided upon
For sPUSCH a flexible design of data symbols and DMRS is considered for the 2os sTTI while for 4os (if adopted) and 7os sTTI, the mapping is determined.
Such flexible design is not appropriate for sPUCCH where multiplexing between sPUCCH UEs and potentially multiplexing between sPUCCH UEs and PUCCH UEs should be possible.

## Slide 3: Proposal
For a given UE the sPUCCH follows a fixed sTTI pattern where the same sTTI boundaries, data symbol placement and DMRS placement are repeated in every subframe. Different fixed mappings apply to different sTTI lengths