## Slide 1: Way Forward on DCI Design of MUST Case 3
MediaTek, ITRI
R1-1613458
3GPP TSG-RAN WG1 #87
Reno, USA, 14th – 18th November 2016
Agenda item 6.2.3.2

## Slide 2: Proposals
For DCI format 2B
  2 bits are added to carry assistance information for predefined antenna port of interfering layer provided in Table 1 of next page
    00: No assistance information
    01: MUST interference is present with QPSK
    10: MUST interference is present with 16QAM
    11: MUST interference is present with 64QAM
For DCI formats 2C and 2D
  When Rel-13-DMRS-table=1, total 4 bits are added to carry assistance information
    2 bits (denoted as B) with the message provided in Table 2 of the next page
    2 bits for MOD of the single interfering layer
      00: Reserved
      01: QPSK
      10: 16QAM
      11: 64QAM
  When otherwise, assistance information is provided in the same ways as DCI format 2B

## Slide 3
Table 1 | 
Antenna port of target UE | Port with assistance information
7 | 8
8 | 7
Note: used when DCI format 2B | 
Table 2 |  |  |  |  |  |  |  | 
Antenna port of target UE | Port with assistance information when OCC length=2 |  |  |  | Port with assistance information when OCC length=4 |  |  | 
 | B=00 | B=01 | B=10 | B=11 | B=00 | B=01 | B=10 | B=11
7 | No assistance information | 8 | Reserved | Reserved | No assistance information | 8 | 11 | 13
8 |  | 7 | Reserved | Reserved |  | 7 | 11 | 13
11 |  | N/A |  |  |  | 7 | 8 | 13
13 |  |  |  |  |  | 7 | 8 | 11
Note: when 00, UE ignores the assistance information of MOD |  |  |  |  |  |  |  |