## Slide 1: Way Forward on Signaling Design of MUST Case 3
MediaTek, CMCC, III, ITRI
R1-1613461
3GPP TSG-RAN WG1 #87
Reno, USA, 14th – 18th November 2016
Agenda item 6.2.3.2

## Slide 2: Proposals
A UE configured with MUST is further configured with a value X in {1, 3} by RRC when Rel-13-DMRS-table=1
  X stands for the maximum number of MUST interfering spatial layers with assistance information in Case 3
  X is smaller than the maximum number of supported layers for spatial multiplexing in DL

## Slide 3: Proposals
For DCI format 2B or Rel-13-DMRS-table=0
  2 bits are added to carry assistance information for predefined antenna port of interfering layer provided in Table 1 of next page
    00: No assistance information
    01: MUST interference is present with QPSK
    10: MUST interference is present with 16QAM
    11: MUST interference is present with 64QAM
For DCI formats 2C and 2D and Rel-13-DMRS-table=1
  When X=1, total 4 bits are added to carry assistance information
    2 bits (denoted as B) with the message provided in Table 2 of the next page
    2 bits for MOD of the single interfering layer
      00: Reserved
      01: QPSK
      10: 16QAM
      11: 64QAM
  When X=3, total 6 bits are added to carry assistance information for predefined ordered antenna ports of interfering layers provided in Table 3 of next page. Two bits for each ordered antenna port. The i-th 2 bits correspond to the i-th predefined antenna port
    Message of each 2 bits are the same as in DCI format 2B

## Slide 4
Table 1 | 
Antenna port of target UE | Port with assistance information
7 | 8
8 | 7
Note: used when DCI format 2B or when X is not configured | 
Table 3 |  |  |  |  | 
Number of layers of desired signal=1 and OCC length=2 |  | Number of layers of desired signal=1 and OCC length=4 |  | Number of layers of desired signal=2 and OCC length=4 | 
Antenna port of target UE | Ordered ports with assistance information | Antenna port of target UE | Ordered ports with assistance information | Antenna ports of target UE | Ordered ports with assistance information
7 | 8, N/A, N/A | 7 | 8, 11, 13 | 7, 8 | 11, 13, N/A
8 | 7, N/A, N/A | 8 | 7, 11, 13 | 11, 13 | 7, 8, N/A
 |  | 11 | 7, 8, 13 |  | 
 |  | 13 | 7, 8, 11 |  | 
Note: used when X=3 |  |  |  |  | 
Table 2 |  |  |  | 
Antenna port of target UE | Port with assistance information |  |  | 
 | B=00 | B=01 | B=10 | B=11
7 | No assistance information | 8 | 11 | 13
8 |  | 7 | 11 | 13
11 |  | 7 | 8 | 13
13 |  | 7 | 8 | 11
Note 1: used when X=1 Note 2: when 00, UE ignores the assistance information of MOD |  |  |  |