## Slide 1: WF on Evaluation Assumptions for Advanced Receivers based on Network Coordination
Samsung, Ericsson, Nokia, Intel, MediaTek, Orange, CeWiT, IITH, IITM, Tejas Networks, …
3GPP TSG RAN WG1 Meeting #87 R1-1613533
Reno, Nevada 14th - 18th November 2016
Agenda Item: 7.1.3.1

## Slide 2: Background
For network coordination aspects, it was agreed in RAN1#86bis that
  Study the need of network assistance and coordination for different types of interference suppression (e.g. inter user, inter-TRP interference) and cancellation based on advanced receivers
  RAN1 to study the following aspects :
    Codeword-to-layer mapping
  This RAN1 study should consider advanced receivers for interference mitigation
    In the case of network coordination: the following can also be studied
      Rank and modulation order
      Modulation mapping

## Slide 3: Background
In R1-1612485, R1-1612486, R1-1612487, R1-1612488, R1-1612489, and R1-1612851, advanced receivers based on network coordination provides significant system throughput improvement at cell edge

## Slide 4: Proposals
For advanced receivers based on network coordination, system-level simulation are encouraged to be evaluated in NR study item
For system-level simulations, urban macro scenario, dense urban scenario excluding small cells, and dense urban scenario including small cells with the same carrier frequency are encouraged to be evaluated in NR study item
Simulation assumptions of TR 38.802 can be a starting point for the evaluation of NR advanced receiver schemes with following refinement:
  Carrier frequency, TP antenna configuration, UE antenna configuration, and UE antenna height
Details on additional information assumed in evaluations should be provided by each company

## Slide 5: SLS Simulation Assumptions (1/3)
Parameters | Urban Macro | Dense urban (Single or Dual layer)
Carrier frequency | 4GHz | Macro layer: 4GHz Small cell layer: 4GHz (co-channel)
Subcarrier spacing | 15kHz | 
System Bandwidth | 20MHz | 
Layout | Hexagonal grid, 3 sectors per site, 19 macro sites (optional: 7 macro sites, similar to that in SCE SI | Macro Layer: Hexagonal grid, 3 sectors per site, 19 macro sites (optional: 7 macro sites, similar to that in SCE SI) Small cell layer: small cells uniformly random dropping within macro geographical area
ISD | 500m | Macro layer: 200m
 |  | Small cell layer: Randomly
Number of Small Cell | - | 3,9 (Optional)
Small cell TP dropping | - | According to TR 38.802
Minimum distances | 35m | 35m for macro cells and 5m for micro cells
Channel model | 3D UMa | 3D UMa (Macro layer) and 3D UMi (Micro layer)
TP Tx power | 49dBm/20MHz | 44dBm/20MHz
TP antenna configuration | (M,N,P,Mg,Ng) = (8,16,2,1,1) (dH,dV) = (0.5, 0.8)λ. | (M,N,P,Mg,Ng) = (8,8,2,1,1) (dH,dV) = (0.5, 0.8)λ.
TP antenna pattern | According to TR 36.873 | 

## Slide 6: SLS Simulation Assumptions (2/3)
Parameters | Urban Macro | Dense urban (Single or Dual layer)
TP antenna height | 25m | 25m for macro cells and 10m for micro cells
UE antenna configuration | Cross Pol (-45/45 degree) | 
UE antenna pattern | Omnidirectional | 
UE antenna height | 1.5m (option 1: calibration purpose), follow 38.802 (option 2: performance evaluation) | 
UE antenna gain | 0 dBi | 
UE receiver noise figure | 9 dB | 
UE Dropping | indoor UE 80%, outdoor UE 20% | 
UE speed | 3km/h | 
UE receiver | Baseline : MMSE-IRC Advanced receiver : advanced receivers can be provided by each company | 
Association of UE to TP | Baseline: RSRP for intra-frequency | 
Transmission scheme | closed-loop rank 1 and 2 SU-MIMO with rank adaptation, open-loop rank 1 and 2 SU-MIMO with rank adaptation (optional), other ranks are not precluded | 
Coordination cluster size for ideal backhaul | Provided by each company | 
Coordinated TP measurement set size | Provided by each company | 
Feedback assumption | Non-ideal CSI-RS/IMR channel/interference estimation (# of CSI ports = 32) | 
Traffic model | Non full buffer FTP traffic model 1, S = 0.1Mbytes (optional) or 0.5Mbytes | 
Traffic load (Resource utilization) | 20%, 40%, 60%, Optional 80% | 
RS modelling | Realistic | 
Channel estimation | Realistic | 

## Slide 7: SLS Simulation Assumptions (3/3)
Parameters | Urban Macro | Dense urban (Single or Dual layer)
Overhead modelling | Realistic | 
Handover margin | 3dB | 
Backhaul link delay | 0ms, 2ms (optional), 5ms, 50ms (optional) | 
Coordination assumptions | Complexity of coordination / information exchange shall be taken into account |