## Slide 1: WF on CSI-RS for beam management
Samsung, NTT DOCOMO, Ericsson, MediaTek
R1-1613570
3GPP TSG RAN WG1 Meeting #87
Reno, USA, 14th - 18th November 2016
Agenda item 7.1.3.3

## Slide 2: Background
RAN1#86bis meeting had the following agreement:
  Working assumptions:
  Beam management procedures can utilize at least the following RS type(s):
    RS defined for mobility purpose at least in connected mode
      FFS: RS can be NR-SS or CSI-RS or newly designed RS
        Others are not precluded
    CSI-RS:
      CSI-RS is UE-specifically configured
        Multiple UE may be configured with the same CSI-RS
      The signal structure for CSI-RS can be specifically optimized for the particular procedure
      Note: CSI-RS can also be used for CSI acquisition
  Other RS could also be considered for beam management such as DMRS and synchronization signals

## Slide 3: Proposal
CSI-RS supports the TRP Tx beam sweeping and UE Rx beam sweeping
The following parameters for CSI-RS transmission can be configured to the UE
  Alt 1:
    NT = 1, 2, ..., NT,Max : Number of time blocks for TRP Tx beam sweeping
    NR = 1, 2, …, NR,Max : Number of time units within each time block for supporting UE Rx beam sweeping
  Alt 2:
    NR = 1, 2, …, NR,Max : Number of time blocks for UE Rx beam sweeping
    NT = 1, 2, ..., NT,Max : Number of time units within each time block for TRP Tx beam sweeping
  NP = 1, 2, …, NP,max: Total number of CSI-RS ports per time unit
    Different CSI-RS ports can correspond to differently steered beams
  For periodic and semi-persistent CSI-RS transmission, periodicity and offset (in terms of slots or subframes).
  Other parameters are not precluded
  FFS:
    Whether explicit or implicit configuration of NT, NR, and NP is supported
    Whether above parameters are configured with one or multiple CSI-RS resource configurations
    CSI-RS resource configuration(s) mechanism, e.g. RRC vs dynamic (L1/L2)
  NOTE: CSI-RS can be used in P1, P2, P3