## Slide 1: WF on Beam Correspondence
Samsung, NTT DOCOMO, InterDigital, MediaTek, Convida Wireless, Sharp, [CATT, Qualcomm]…
R1-1613542
3GPP TSG RAN WG1 Meeting #87
Reno, USA, 14th - 18th November 2016
Agenda item 7.1.3.3

## Slide 2: Background (1/2)
Working assumption:
  The followings are defined as Tx/Rx beam correspondence at TRP and UE :
    Tx/Rx beam correspondence at TRP holds if at least one of the following is satisfied:
      TRP is able to determine a TRP Rx beam for the uplink reception based on UE’s downlink measurement on TRP’s one or more Tx beams.
      TRP is able to determine a TRP Tx beam for the downlink transmission based on TRP’s uplink measurement on TRP’s one or more Rx beams
    Tx/Rx beam correspondence at UE holds if at least one of the following is satisfied:
      UE is able to determine a UE Tx beam for the uplink transmission based on UE’s downlink measurement on UE’s one or more Rx beams.
      UE is able to determine a UE Rx beam for the downlink reception based on TRP’s indication based on uplink measurement on UE’s one or more Tx beams.
    More refined definition can still be discussed

## Slide 3: Background (2/2)
Agreements:
UL beam management is to be further studied in NR
  Similar procedures can be defined as DL beam management with details FFS, e.g.:
    U-1: is used to enable TRP measurement on different UE Tx beams to support selection of UE Tx beams/TRP Rx beam(s)
      Note: this is not necessarily useful in all cases
    U-2: is used to enable TRP measurement on different TRP Rx beams to possibly change/select inter/intra-TRP Rx beam(s)
    U-3: is used to enable TRP measurement on the same TRP Rx beam to change UE Tx beam in the case UE uses beamforming
FFS Indication of information related to Tx/Rx beam correspondence is supported
Study UL beam management based on:
  PRACH
  SRS
  DM-RS
  Other channels and reference signals are not precluded
Study uplink beam management procedure by considering the Tx/Rx beam correspondence
  For the case of TRP and UE have Tx/Rx beam correspondence
  For the case of TRP has no Tx/Rx beam correspondence and/or UE has no Tx/Rx beam correspondence

## Slide 4: Proposal
Study whether or not procedure(s) for determining UE’s capability on beam correspondence is needed.
  e.g. the procedure may include comparison between feedback from TRP and reciprocity/correspondence based beam determination
  the study may consider the following aspects -
    e.g. metrics to be considered SNR/Power (beam-quality), CSI, and others
    e.g. values of the metrics at which beam correspondence is declared
Support reporting to the gNB about beam correspondence at the UE
  FFS: signalling mechanisms

## Slide 5: Appendix
Example procedure for determining beam correspondence
  Step1: Tx beam sweeping
  Step2: Inform selected beam information based on Step1
    e.g., beam index is signaled
  Step3: Reciprocity based Rx beam selection
  Step4: Compare selected beams in steps 2 and 3 and judge correspondence