## Slide 1: WF on QCL issues for eFD-MIMO
LG Electronics, CATT, Ericsson, NTT DOCOMO, Qualcomm, Samsung, [AT&T, ITL, KT Corporation, Mitsubishi Electric, Nokia, Alcatel-Lucent Shanghai Bell, Xinwei]
R1-1613734
3GPP TSG RAN1 #87
Reno, USA, Nov. 14 – 18, 2016
Agenda Item: 6.2.2.4.1.

## Slide 2: Conclusion from email discussion [86b-10] on QCL assumptions

## Slide 3: Proposal
In TM10, NZP CSI-RS activation/deactivation with subframe_config can be configured with UEs configured with QCL Type B, where
  NZP CSIRS configured for activation/deactivation with subframe_config can be indicated in PQI for QCL purpose, and follow legacy QCL assumption.
    UE does not expect to receive PQI indication before receiving X(>1) activated NZP CSI-RSs from an NZP CSIRS activation. FFS on X.
    UE does not expect that a PQI indication is received which indicates a deactivated NZP CSI-RS. FFS the spec impact.
    Note: NZP CSI-RS not configured for activation/deactivation can also be indicated for QCL purpose.