## Slide 1: WF on Remaining issues on DCI design for SC-MCCH for multicast in FeMTC
Ericsson, Nokia, ABS…
R1-1703802
3GPP TSG-RAN WG1 Meeting #88
Athens, Greece, 13th – 17th February 2017Agenda item 7.2.3.2

## Slide 2: Background
In RAN1#87 meeting, regarding SC-PTM in FeMTC, the followings are agreed:
MPDCCH search space configuration for SC-MCCH consists of {narrowband, Rmax, G}.
MPDCCH search space configuration for SC-MTCH consists of {narrowband, Rmax, G}.
For the MPDCCH search space scheduling SC-MCCH, UE monitoring of blind decoding candidates is reused from Type1-CSS.
For the MPDCCH search space scheduling SC-MTCH, UE monitoring of blind decoding candidates is reused from Type2-CSS.
DCIs for scheduling SC-MCCH is based on DCI format 6-2 with at least the following fields:
    Resource assignment
    Number of PDSCH repetitions
    MCS
    Number of MPDCCH repetitions
The sizes of the DCI fields are FFS.
Other DCI fields than the ones listed above are not precluded.

## Slide 3: Background
Currently, the Number of PDSCH repetitions field in the DCI has not defined for SC-MCCH

## Slide 4: Proposal
It is proposed to consider one of the following alternatives for the definition of SC-MCCH DCI PDSCH “Repetition number”
  Alt1: Same as paging (Table 7.1.11-3 in TS 36.213), i.e., condition on the DCI subframe repetition number
  Alt 2: The subset of repetitions that the SC-MCCH DCI PDSCH “Repetition number” field refers to, is indicated by the 1 bit CE mode indication bit as
    CE mode A: [2,4,8,16,32,64,128,256]
    CE mode B: [16,32,64,128,256,512,1024, 2048]
  Alt 3: Use 3 bits to indicate 8 different values as follows.
    [4,8,32,64,128,512,1024,2048]