## Slide 1: WF on multiple slots design for PUCCH in long duration
Huawei, HiSilicon, OPPO, vivo, Panasonic, CMCC, NTT DOCOMO…
3GPP TSG-RAN WG1 Meeting #88
Athens, Greece, 13th-17th February 2017
AI: 8.1.3.2.2
R1-1703861

## Slide 2: Background
Agreements:
A UCI carried by long duration UL control channel at least with low PAPR design can be transmitted in one slot or multiple slots
  Transmission across multiple slots should allow a total duration of [1] ms at least for some cases
    FFS: more than [1] ms at least for some cases
  FFS the numbers of the slots
Agreements
Long UL-part of a slot can be used for transmission of PUCCH in long-duration
  i.e., PUCCH in long-duration is supported for both UL-only slot and a slot with the number of uplink symbols greater than X (X >= 2).
    FFS exact value of X

## Slide 3: Proposal
For PUCCH in long duration on multiple slots,
  A UCI is repeatedly transmitted in N slots is supported. (N>1)
    FFS a UCI can be jointly encoded for N slots
    The N slots may not be adjacent
    The indicated N slots can be multiple UL-only slots or multiple bi-directional slots, or combination of UL-only slots and bi-directional slots
    How to explicitly or implicitly indicate N is FFS
FFS a long PUCCH in one slot is realized by the repetition/combination of PUCCHs