## Slide 1: WF on Modulation for NR UL
MediaTek, Qualcomm, Samsung, AT&T, Xiaomi, DISH Network, Thales, Idaho National Lab, Hughes Network Systems, IITH, CEWiT, IITM, Tejas Networks, NTU
3GPP TSG RAN WG1 Meeting #88 R1-1704045
Athens, Greece, 13th – 17th February 2017
Agenda item: 8.1.5

## Slide 2: Background
Agreement (RAN1 NR Ad-Hoc, Spokane, USA)
  NR supports 0.5*pi BPSK modulation for DFT-s-OFDM
Working Assumption
  While using DFT-s-OFDM, 0.5*pi-BPSK modulation using DFT-S-OFDM with frequency domain spectrum shaping can be further considered at least for eMBB uplink data for up to 40GHz
  FFS
    The details of frequency domain spectrum shaping
    This does not preclude the case where no spectrum shaping is needed

## Slide 3: Low PAPR Q & A
Q: What could low PAPR modulations offer for NR?
  Due to the expected stricter spectral requirements (e.g., ACLR, OOBE), there are more cases in NR (compared with LTE) where low PAPR modulations could provide coverage extension [1].
  With modern PA technologies (e.g., envelope tracking), low PAPR modulations could provide significant UE power saving when compared to conventional QPSK at the same PA output power [1].
[1] R1-1702729, “Low PAPR Modulation Design for NR UL,” MeidaTek Inc.

## Slide 4: Concerns & Solutions
What’s the major concern of the currently proposed low PAPR modulations?
  Limitation of π/2-BPSK without FDSS @ spectral efficiency > 0.5 bit/s/Hz
    For π/2-BPSK without Frequency Domain Spectral Shaping (FDSS), the MCL advantage over QPSK vanishes as spectral efficiency increases [1][2].
Is there any solution to this low spectral efficiency issue?
  QPSK based low PAPR modulation could achieve high MCL gain @ spectral efficiency > 0.5 bit/s/Hz
    Even without FDSS, the interpolated-QPSK, a special case of low PAPR TCM design, provides MCL gain of 0.8dB across a wide spectrum of spectral efficiency, ranging from 0.25 bit/s/Hz to 1.25 bit/s/Hz [1].
    With FDSS, significant PAPR reduction could be obtained with rotated-QPSK [3].
[2] R1-1701039, “Rotated modulations for DFT-S-OFDM uplink,” Nokia, Alcatel-Lucent Shanghai Bell.
[3] R1-1701000, “Performance evaluation results of DFT-s-OFDM with FDSS,” Samsung.

## Slide 5: Proposals
NR Supports QPSK based low PAPR modulation for DFT-s-OFDM