## Slide 1: WF on the retuning of SRS transmission
Huawei, HiSilicon, Ericsson…
R1-1704046
3GPP TSG-RAN WG1 Meeting #88
Athens, Greece, 13th – 17th February 2017
Agenda item 7.2.3.1.5

## Slide 2: Proposal 1
For a Rel-14 BL UE, if SRS is transmitted on the last symbol in special subframe n, and if the SRS transmission bandwidth is not completely within the frequency resource of PUCCH/PUSCH in subframe n+1:
  If the UE needs one symbol for retuning, then:
    When retuning between SRS and PUCCH, the guard period is the last symbol in special subframe n
    When retuning between SRS and PUSCH, the guard period is the first SC-FDMA symbol of PUSCH in subframe n+1
  If the UE needs two symbols for retuning, then:
    When retuning between SRS and PUCCH, the guard period is the last symbol in special subframe n and the first symbol of PUCCH in subframe n+1
    When retuning between SRS and PUSCH, the guard period is the first two SC-FDMA symbols of PUSCH in subframe n+1

## Slide 3: Proposal 2
For a Rel-14 BL UE, if the last SRS symbol in special subframe n is the last but one symbol in that subframe, and if the SRS transmission bandwidth is not completely within the frequency resource of PUCCH/PUSCH in subframe n+1:
  If the UE needs one symbol for retuning, then:
    When retuning between SRS and PUCCH/PUSCH, the guard period is the last symbol in special subframe n
  If the UE needs two symbols for retuning, then:
    When retuning between SRS and PUCCH/PUSCH, the guard period is the last symbol in special subframe n and the first symbol of PUCCH/PUSCH in subframe n+1

## Slide 4: Proposal 3
For a Rel-14 BL UE, if SRS is transmitted on the first UpPTS symbol in special subframe n, and if the SRS transmission bandwidth is different from frequency resource of DwPTS reception in subframe n:
  If the UE needs one/two symbol(s) for retuning, then:
    The guard period is the last one/two symbol(s) in DwPTS reception

## Slide 5: Proposal 4
For a Rel-14 BL UE, if the first symbol for SRS transmission in special subframe n is the second UpPTS symbol in subframe n, and if the SRS transmission bandwidth is different from frequency resource of DwPTS reception in subframe n:
  If the UE needs one symbol for retuning, then:
    The guard period is the first UpPTS symbol
  If the UE needs two symbols for retuning, then:
    The guard period is created by the last DwPTS symbol and the first UpPTS symbol