## Slide 1: WF on DCI size for max 5 MHz PDSCH resource allocation in CE mode A
ZTE, ZTE Microelectronics, Qualcomm, …
3GPP TSG RAN WG1 Meeting #88 R1-1704054
Athens, Greece 13th - 17th February 2017
Agenda Item: 7.2.3.1.1

## Slide 2: Background
For PDSCH resource allocation for 5 MHz in CE mode A:
    ‘Starting narrowband index’ is used to indicate the overlapped wideband.
    ‘Narrowband bitmap within the wideband + resource allocation within the narrowband’ is used to indicate the resource allocation within the wideband.

## Slide 3: Proposal
  Size of ‘Starting narrowband index’ is .
  ‘Narrowband bitmap within the wideband’ is 3 bits to indicate the allocation of other 3 narrowbands excluding the starting narrowband. (The starting narrowband is always assumed to be allocated)
  ‘Resource allocation within the narrowband’ is 5 bits, as same as in Rel-13 eMTC where DL resource allocation type 2 is used.