## Slide 1: WF on DL signals for random access
ZTE, ZTE Microelectronics,
3GPP TSG RAN WG1 Meeting #88bis
Spokane, USA, 3rd – 7th April 2017
Agenda: 8.1.1.4.2
R1-1706552

## Slide 2: Background
NR supports association between DL signals/channels and subset of RACH resources/preambles.
NR supports CSI-RS for L3 mobility
CSI-RS for L3 mobility can provide efficient RRM measurement of many TRPs and narrow beams , e.g. with single SS-block transmitted with SFN
Supporting association between CSI-RS for L3 mobility and subset of RACH resources/preambles can provide high gain beamforming of Msg1-4

## Slide 3: Proposal
Either IDLE mode RS or CSI-RS for L3 mobility can be used as DL signals/channels for selection of subset of RACH resource and/or subset preamble indices, at least for CONNECTED mode.
  FFS using CSI-RS in IDLE mode random access, by informing configuration of CSI-RS for L3 mobility together with random access configuration
  Note that how a UE can obtain the configuration of CSI-RS for L3 mobility is for further discussion in other agenda items.