## Slide 1: WF on DL CORESET configuration
OPPO, Ericsson, Panasonic, ZTE, CATT, Intel
3GPP TSG RAN WG1 Meeting #89 Hangzhou, P.R. China 15th – 19th May 2017
Agenda item: 7.1.3.1.2
R1-1709266

## Slide 2: Background
RAN1#87 agreement
  At least for single-stage DCI design:
    A control resource set (formerly called control subband) is, in the frequency domain, a set of PRBs within which the UE attempts to blindly decode downlink control information
      The PRBs may or may not be frequency contiguous
      A UE may have one or more control resource sets
      Working assumption: One DCI message is located within one control resource set
  In frequency-domain, a PRB is the resource unit size (may or may not including DM-RS) for control channel
  when the control resource set spans multiple OFDM symbols, NR support a control channel candidate to be mapped to multiple OFDM symbols or to a single OFDM symbol
    The gNB can inform UE which control channel candidates are mapped to each subset of OFDM symbols in the control resource set. FFS: details of the signaling (implicit or explicit)

## Slide 3: Proposal
In time domain, a CORESET can be configured with one or a set of contiguous OFDM symbols
  The configuration indicates the starting OFDM symbol and time duration
Support 1-3 OFDM symbol as time duration for a CORESET
  FFS: Other time duration
  FFS: The relation between time duration and CCE-to-REG mapping
  FFS: Relationship of a first PDSCH DMRS symbol with one or more symbols of a CORESET for slot-based scheduling
A CORESET is configured with only one CCE-to-REG mapping