## Slide 1: WF on group-based beam reporting
3GPP TSG RAN WG1 Meeting #89 R1-1709307
Hangzhou, P.R. China 15th – 19th May 2017
Agenda Item: 7.1.2.2.1
ZTE, ASTRI, Nokia, ASB, Samsung, NTT DOCOMO, Qualcomm

## Slide 2: Background
  The following agreements on grouping-based beam reporting been reached:
    Alt 1:
  - UE reports information about TRP Tx Beam(s) that can be received using selected UE Rx beam set(s) where a Rx beam set refers to a set of UE Rx beams that are used for receiving a DL signal.
    - NOTE: Different TRP Tx beams reported for the same Rx beam set can be received simultaneously at the UE.
    - NOTE: Different TRP TX beams reported for different UE Rx beam set may not be possible to be received simultaneously at the UE
Alt 2:
  - UE reports information about TRP Tx Beam(s) per UE antenna group basis where UE antenna group refers to receive UE antenna panel or subarray.
    - NOTE: Different TX beams reported for different antenna groups can be received simultaneously at the UE.
    NOTE: Different TX beams reported for the same UE antenna group may not be possible to be received simultaneously at the UE

## Slide 3: Background
  The following agreements on details of grouping-based beam reporting have been reached:
    NR supports the following beam reporting considering L groups where L>=1 and each group refers to a Rx beam set (Alt1) or a UE antenna group (Alt2) depending on which alternative is adopted.
    - For each group l, UE reports at least the following information:
      Information indicating group at least for some cases
      Measurement quantities for Nl beam (s)
        Support L1 RSRP and CSI report (when CSI-RS is for CSI acquisition)
      Information indicating Nl DL Tx beam(s) when applicable
    - This group based beam reporting is configurable per UE basis.
      This group based beam reporting can be turned off per UE basis e.g. when L=1 or Nl=1
        NOTE: No group identifier is reported when it is turned off

## Slide 4: Background
  The following agreements on further evaluation of grouping-based beam reporting have been reached:
    For beam reporting, companies are encouraged to perform detailed analysis w.r.t. comparing Alt 1 and Alt 2, particularly considering the overhead (feedback overhead, signaling overhead, etc.), performance, flexibility in operation, etc.
      Aim to down-select one of the two alternative s with the possibility of merging into a single alternative (if so, the corresponding analysis) at next meeting
      Each company to state the assumed UE implementation in the analysis

## Slide 5: Proposal
  NR supports Alt. 1 of group based beam reporting (i.e., UE reports information about TRP Tx Beam(s) that can be received using selected UE Rx beam set(s) where a Rx beam set refers to a set of UE Rx beams that are used for receiving a DL signal)
    Study further interpretation of Tx beams within one group referring to a Rx beam set (Alt1) and its potential sub-categories, e.g.,
      Refinement of beam group definition e.g.
        different TRP TX beams reported for different UE Rx beam set may not be possible to be received simultaneously at the UE
        different TRP TX beams reported for different UE Rx beam set cannot be possible to be received simultaneously at the UE
      UE assistant to transmission scheme selection
        received simultaneously but not for spatially multiplexing
        received simultaneously and for spatially multiplexing
      FFS: spec impact, e.g., multi-level grouped by UE or provisioned by gNB, multi-stage reporting of grouping information