## Slide 1: WF on beam recovery
3GPP TSG RAN WG1 Meeting #89 R1-1709309
Hangzhou, P.R. China 15th – 19th May 2017
Agenda Item: 7.1.2.2.2
ZTE, MediaTek, vivo, Spreadtrum, Qualcomm, ASTRI, AT&T, OPPO, Ericsson, LGE, Xinwei, [Interdigital, Samsung]

## Slide 2: Background
The following agreements on beam recovery have been reached:
  Beam failure detection
    UE monitors beam failure detection RS to assess if a beam failure trigger condition has been met
    Beam failure detection RS at least includes periodic CSI-RS for beam management
      SS-block within the serving cell can be considered, if SS-block is also used in beam management as well
    FFS: Trigger condition for declaring beam failure
  New candidate beam identification
    UE monitors beam identification RS to find a new candidate beam
      Beam identification RS includes
        Periodic CSI-RS for beam management, if it is configured by NW
        Periodic CSI-RS and SS-blocks within the serving cell, if SS-block is also used in beam management as well
  Beam failure recovery request transmission
    Information carried by beam failure recovery request includes at least one followings
      Explicit/implicit information about identifying UE and new gNB TX beam information
      Explicit/implicit information about identifying UE and whether or not new candidate beam exists
      FFS:
        Information indicating UE beam failure
        Additional information, e.g., new beam quality
    Down-selection between the following options for beam failure recovery request transmission
      PRACH
      PUCCH
      PRACH-like (e.g.,different parameter for preamble sequence from PRACH)
    Beam failure recovery request resource/signal may be additionally used for scheduling request
  UE monitors a control channel search space to receive gNB response for beam failure recovery request

## Slide 3: Proposal
  In addition to periodic CSI-RS, SS-block within the serving cell can be used for the following aspect:
    New candidate beam identification
      FFS: combination of SS block and periodic CSI-RS resources can be used together for identifying candidate beams.
  Notes: Periodic CSI-RS has been agreed for new candidate beam identification
  Notes: UE-specifically configured CSI-RS has been supported in NR.