## Slide 1: WF on DMRS port to layer mapping for NC-JT
Ericsson, Huawei, HiSi, [Intel],[Samsung] …
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th – 19th May 2017
Agenda item 6.2.4.1
R1-1709316

## Slide 2: Background
DMRS port groups 7/8/11/13 and 9/10/12/14 occupy orthogonal frequency resources while CDM is used within the port groups
Channel estimation with CDMed ports can become problematic if ports have different power level, e.g. by being transmitted from different TPs
Consecutive DMRS port numbers are assigned to layers according to current Antenna port(s), scrambling identity and number of layers indication in DCI
The first layers are mapped to the first codeword while the remaining layers are mapped to the second codeword
  The second CW always has more than or equally many layers as the first CW
Two Codewords: Codeword 0 enabled, Codeword 1 enabled | 
Value | Message
0 | 2 layers, ports 7-8, nSCID=0
1 | 2 layers, ports 7-8, nSCID=1
2 | 3 layers, ports 7-9
3 | 4 layers, ports 7-10
4 | 5 layers, ports 7-11
5 | 6 layers, ports 7-12
6 | 7 layers, ports 7-13
7 | 8 layers, ports 7-14

## Slide 3: Proposal
When NC-JT transmission is indicated in PQI, the following DMRS port to layer mapping is used
  Note: This implies that layers corresponding to different CWs are mapped to FDMed DMRS ports for rank 3-8. Rank-2 port mapping is the same as legacy to maintain DMRS overhead.
Rank | DMRS-to-layer mapping | 
 | DMRS group 1 (CW1) | DMRS group 2 (CW2)
1 | N/A | 
2 | 7 | 8
3 | 7 | 9,10
4 | 7,8 | 9,10
5 | 7,8 | 9,10,12
6 | 7,8,11 | 9,10,12
7 | 7,8,11 | 9,10,12,14
8 | 7,8,11,13 | 9,10,12,14