## Slide 1
3GPP TSG-RAN WG1 #89 R1-1709360
Hangzhou, China, 15th – 19th May 2017
Agenda: 7.1.2.1.1
WF on CW to layer mapping scheme for data channels
Qualcomm, Samsung, Panasonic, Intel, Sharp,
Ericsson, CATT, KDDI, Interdigital, ATT, Nokia, ASB

## Slide 2: Background
Codeword to layer mapping scheme:
  Due to early-decoding-constraints layer mapping over frequency should be prioritized over time.
  Mapping across layers of each codeblock provides spatial diversity
UL transmission with DFT-SOFDM waveform is only applicable to single-layer/stream transmission

## Slide 3: Proposals
For UL data channel with CP-OFDM waveform and DL data channel, the modulated symbol stream associated with a codeword is mapped to the allocated resource in the following manner:
  first across layers associated with the codeword, then across subcarriers (frequency) and then across OFDM symbols (time).