## Slide 1: WF on SRS Tx beam determination
LG Electronics, Intel Corporation
R1-1709376
3GPP TSG RAN1 #89
Hangzhou, P.R. China, 15th – 19th May 2017
Agenda Item: 7.1.2.2.1

## Slide 2: Background and Motivation
Agreements in RAN1#88
Purpose of this WF is to further agree on the necessary details of the agreed Alt.2, according to the following two cases:
  When UE beam correspondence is hold
  When UE beam correspondence is not hold

## Slide 3: Proposals
When UE beam correspondence is hold,
  NR supports a DL RS indication for a configured SRS resource, where the SRS Tx beam should correspond to DL Rx beam used for receiving the indicated DL RS.
    The DL RS indication can be CRI(CSI-RS resource indicator), at least.
    FFS: The indication via MAC CE and/or DCI
When UE beam correspondence is not hold,
  NR supports a UL RS indication for a configured SRS resource, where UE transmits the SRS using the beam used for transmitting the indicated UL RS.
    The UL RS indication can be SRI(SRS resource indicator), at least.
    FFS: The indication via MAC CE and/or DCI

## Slide 4: Proposals
In case when no explicit Tx beam indication is provided for a configured SRS resource for UL beam management,
  it is supported that the UE may transmit the SRS using the beam used for Msg.3.
In case when UE is not configured with any SRS resources,
  it is supported that the UE may transmit PUSCH using the beam used for Msg.3.