## Slide 1: WF on Random access configuration
ZTE
3GPP TSG RAN WG1 Meeting #89
Hangzhou, USA, 15th – 19th May 2017
Agenda: 7.1.1.4.2
R1-1709416

## Slide 2: Background
Agreements (RAN1#88bis):
Association between one or multiple occasions for SS block and a subset of RACH resources and/or subset of preamble indices is informed to UE by broadcast system information or known to UE or FFS dedicated signaling
  FFS gNB can configure an association between CSI-RS for L3 mobility and a subset of RACH resources and/or a subset of preamble indices, for determining Msg2 DL Tx beam

## Slide 3: Background
There is no need to define PRACH resources associated with SS blocks that are not transmitted.
UE always assuming L SS blocks can give longer PRACH delay.
1
2
3
L
...
Nominal SS blocks (L=64)
PRACH 1
PRACH 2
PRACH L (64)
PRACH 1
Maximum PRACH delay
1
2
3
...
Actually transmitted SS blocks (4)
PRACH 1
PRACH 2
PRACH 1
Maximum PRACH delay
4
PRACH 3
PRACH 4
...
...

## Slide 4: Proposal
Random access (RA) configuration is included in remaining minimum SI.
Support RA association based on both
  maximum number of SS blocks (for the frequency carrier) and
  the actually transmitted SS blocks.
Indication of actually transmitted SS blocks can be included in remaining minimum SI.
Note: If indication of actually transmitted SS blocks is not included in remaining minimum SI, then the RA association is based on the maximum number of SS blocks.
Note: This does not preclude a dedicated configuration of PRACH resources, RA association and/or indication of actually transmitted SS blocks for CONNECTED mode UEs.