## Slide 1: WF on Repeating Coded Bits of Polar Code
Ericsson, ZTE, MediaTek, Qualcomm, InterDigital
R1-1709464
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th – 19th May 2017
Agenda item 7.1.4.2.1.2

## Slide 2: Background (1)
Working Assumption for UCI (from RAN #88):
Nmax,UCI =1024
  Optimise code design for K up to 200
    Also aim for code design that supports values of K up to 500 with good performance, typically using higher code rates
      Without prejudice to the final design, companies are encouraged to investigate advanced code rate matching schemes until RAN1#88bis
Working assumption can be revisited at RAN1#88bis if it does not prove to be possible to generate a good code design with Nmax,UCI =1024

## Slide 3: Background (2)
Several companies have independently observed that performance of repetition is fine if a proper subset of coded bits to be repeated is chosen. For examples,
  R1-1704319 Performance Study of Extended Polar Code, Ericsson
  R1-1704460 Comparison and optimization of Polar code rate matching, MediaTek
  R1-1705634 A comprehensive Rate-matching scheme for polar code and performance evaluation, Qualcomm
  R1-1705423 Repetition for polar codes, Samsung

## Slide 4: Proposal
Confirm Working Assumption:
  Maximum code size, Nmax=2n, at the output of Polar encoding for Uplink Control Information (UCI) is:
    Nmax,UCI = 1024 for uplink control information
If the desired code block length M is larger than Nmax, subset of code bits at the output of Polar encoder is repeated as the extra (M- Nmax ) code bits
  If code block segmentation is applied, for constituent Polar code j, desired code block length M refers to Mj at the output of constituent Polar encoder j
  FFS: how to select the subset of code bits to repeat
  FFS: if/how repetition can be applied when M< Nmax