## Slide 1: WF on Early data transmission for MTC
Ericsson, Huawei, HiSilicon
3GPP TSG-RAN WG1 Meeting #89
Hangzhou, China, May 15-19, 2017
Agenda item 6.2.6.6
R1-1709469

## Slide 2: Background
Some potential issues related to other WGs have been identified
  Early data in Msg2 may be inefficient (multiple UEs, multiple cells, multiple coverage levels)
  Currently small grant sizes (LTE-MTC) or fixed grant sizes (NB-IoT) for Msg3 given in RAR
  Potential RAN2 impacts
    Grant mechanism for Msg3, larger grants /dual grants
    If and how (N)PRACH is partitioned for indication of early data support
    How user data is multiplexed
    Security issues (also SA3)
    UE ID (before Msg4) and UE capabilities are not available to eNB

## Slide 3: Proposal
Early data transmission should be available to UEs with any CE level or coverage
Early data in Msg2 is not supported for contention-based RA
In uplink, specify early data transmission in Msg3
In downlink, specify early data transmission in Msg4