## Slide 1
3GPP TSG RAN WG1 Meeting RAN1#89 R1-1709490
Hangzhou, P.R. China 15th – 19th May 2017
Agenda item: 7.1.1.1.3
WF on SS Block Index Indication
Samsung, Sony, ITL, Fujitsu, …

## Slide 2: Background
The following agreements were achieved in RAN1 #88bis,
Agreements:
  PSS sequence length: 127 for frequency domain-based pure BPSK M sequence
    Note that PSS will be mapped to consecutive 127 subcarriers
  SSS sequence length: 127
  Subcarrier spacings for PSS/SSS for difference freq. ranges: 15kHz/30kHz for below 6 GHz, and 120kHz/240kHz for above 6 GHz
    Note: RAN1 assumes that RAN4 will decide it depending on frequency ranges
  SS burst set periodicity default value for initial cell selection: 20/20 msec
    Note that RAN1 assumes that RAN4 will investigate requirements
  Time index indication: PBCH conditioned that mobility and HO related requirements can be met
    Note: RAN1 assumes that RAN2 will check against to RAN2 requirements
  PBCH BW: 288 subcarriers, 2 OFDM symbols (additional symbols if MIB size larger than assumed)
  PBCH phase reference: DMRS
  PBCH TTI: 80 msec

## Slide 3: Discussion
RAN1 agreed that PBCH TTI is 80 msec
  PBCH contents (MIB) are the same within 80 msec
  This agreement allows PBCH soft combining within the PBCH TTI, and it is helpful for UE achieving good decoding performance
RAN2 conclusion on the RAN1 LS in the Spokane meeting:
  RAN2 understand that receiving Time index indication from PBCH could violate the RAN2 principle that UE is not required to receive system information from a neighbour cell to perform measurements.
Explicit/implicit SS block index indication based on NR-PBCH decoding causes high UE complexity/latency of PBCH decoding for neighbor cells during cell searching and RRM measurement

## Slide 4: Proposal
Down select the scheme for NR-SS block index indication
  Option 1: DMRS in PBCH is utilized to indicate the SS block indices in a SS burst set
    FFS on the DMRS sequence/resource design
  Option 2: DMRS in PBCH is utilized to indicate the NR-SS block indices in a SS burst
    FFS definition of SS burst (e.g., maximum number of SS blocks within SS burst)
    FFS on the indication of SS burst indices in a SS burst set
    FFS on the DMRS sequence/resource design