## Slide 1: WF on HARQ combining for UL URLLC without grant
LG Electronics, Panasonic, Huawei, HiSilicon, Sony
3GPP TSG RAN1 #89
Hangzhou, P.R. China May 15th – 19th, 2017
Agenda Item: 7.1.3.3.2
R1-1709510

## Slide 2: Background
For UE configured with K repetitions for a TB transmission with/without grant, the UE can continue repetitions (FFS can be different RV versions, FFS different MCS) for the TB until one of the following conditions is met
  If an UL grant is successfully received for a slot/mini-slot for the same TB
    FFS: How to determine the grant is for the same TB

## Slide 3: Proposal
Soft combining between initial TB transmission without grant and retransmission of the same TB with grant is supported.
  There is a mapping rule between the ID used in grant-free UL transmission and ID used in UL grant
    FFS: details of the mapping rule (e.g. based on time/frequency resource and RS sequence)
    FFS: details of ID used in grant-free UL
    FFS: details of ID used in UL grant
  Mechanisms to determine the parameter(s) associated with a TB (e.g. NDI, HPN, RV) is supported
FFS: More than one HARQ processes are supported for UL transmission without grant