## Slide 1: WF on CSI Measurement Details
NTT DOCOMO, Nokia, ASB, Samsung, …
3GPP TSG RAN WG1 Meeting #89
Hangzhou, P.R. China 15th – 19th May 2017
Agenda item: 7.1.2.3.2
R1-1709515

## Slide 2: Background
Agreements from RAN1 #88bis
Agreements:
For interference measurement, down selection from options will be conducted.
NZP CSI-RS based
  Opt. A1: Estimation on NZP CSI-RS for channel estimation (by subtracting CSI-RS from Rx signal)
  Opt. A2: Emulation on NZP CSI-RS which is represented by multiplied value of channel and precoding matrix
DM-RS based
  Opt. B1: Estimation on DM-RS for own data demodulation (by subtracting DM-RS from Rx signal)
  Opt. B2: Estimation on DM-RS for other UEs
Criteria for design and down selection are as follows.
  Required RS densities
  UE processing latency
  Support of self-contained CSI reporting (if supported) at least depends on the location of IMR.
FFS: Whether the emulation is performed at TRP side or UE side
FFS: RAN1 specification impact, if any, on the options above

## Slide 3: Proposal
NR supports interference measurement on multiple resources from ZP CSI-RS, NZP CSI-RS, and DMRS.
  For NZP CSI-RS based measurements, the detailed schemes can be down-selected from Option A1 and A2.
  For DMRS based measurements, the detailed schemes can be down-selected from Option B1 and B2.
NR supports aperiodic/semi-persistent CSI report with multiple interference measurement resources.