## Slide 1: WF on UL HARQ-ACK feedback
ZTE , Nubia, Huawei, HiSilicon, Ericsson, Lenovo, …
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th - 19th May 2017
Agenda item 6.2.6.3
R1-1709541

## Slide 2: Background
Early PUSCH termination can be realized by UL grant for scheduling new data if eNB has new UL data to be scheduled. In this case, UL grant for scheduling new data is transmitted in advance, and no additional overhead for HARQ-ACK feedback is caused.
Early PUSCH termination can be realized by a new ACK feedback channel if eNB has no UL data to be scheduled.
For new HARQ-ACK feedback channel using PHICH-like structure, new physical resource for HARQ-ACK feedback needs to be reserved which would reduce the available resources for MPDCCH and PDSCH. Besides, the standardization effort is increased.

## Slide 3
Proposal 1
  UL HARQ feedback based on MPDCCH is supported.
  MPDCCH for implicit HARQ-ACK feedback by UL grant for scheduling new UL data transmission for the same HARQ process ID
  MPDCCH for explicit HARQ-ACK feedback if there is no new UL data being scheduled for the same HARQ process ID
  Early PUSCH termination is supported for FD-FDD and TDD.
    FFS for HD-FDD