## Slide 1: WF for UL DMRS position for 2os TTI for DMRS multiplexing/sharing
Ericsson, LG Electronics
R1-1709628
3GPP TSG RAN1 #89
Hangzhou, China, 15th - 19th May 2017
Agenda item 6.2.1.2.1.2

## Slide 2: Background (1/2)
In the work item description [1], for Frame structure type 1, it is proposed to
  Specify support for a transmission duration based on 2-symbol sTTI, 4-symbol sTTI, and 1-slot sTTI for sPUCCH/sPUSCH
  Down-selection is not precluded
Based on the outcome of the study item on latency reduction [2], the followings are recommended to be supported for the design of DMRS for sPUSCH:
  For the case of 1-slot TTI length, reuse the current DM-RS
  For the case of less than 1-slot TTI length, support DM-RS sharing/multiplexing of consecutive TTIs from one or multiple UEs
  At least 2 contiguous TTIs can be shared/multiplexed.
In RAN1#88, it has been agreed that for 2-OS sTTI, the UL sTTI pattern for sPUSCH is (3,2,2,2,2,3).

## Slide 3: Background (2/2)
The following agreement was made in RAN1#88bis to cover the case where UL DMRS is contained in the scheduled UL sTTI
  Agreement:
    For 2/3-symbol sPUSCH transmission, at least the following configurations are supported and one of the configurations for sTTI#n+x is indicated by the UL grant at sTTI#n, if the scheduled sTTI#n+x includes both data and the associated RS, where x is processing time
      sTTI#n+x = sTTI#0: {R D D}, FFS:{D D R}, FFS: {D R D}
      sTTI#n+x = sTTI#1,2,3,4: {R D}, FFS: {D R}
      sTTI#n+x = sTTI#5: {R D D}, FFS: {D R D}
        FFS if data in the last symbol can be transmitted in cell specific SRS subframes
      Other configurations are not precluded
    FFS for the case where data and associated RS are in different sTTIs

## Slide 4: Proposal
To enable robust DMRS sharing and DMRS multiplexing in case of a RRC configured TTI length of 2os in UL, the following DMRS placement can be indicated by an UL grant in sTTI#n-x which schedules sPUSCH in sTTI n, where x is processing time configured for a PUCCH group
  sTTI 0 (i.e. n = 0): DDR
  sTTI 1 (i.e. n = 1): DD|R
  sTTI 3 (i.e. n = 3): DD|R
  sTTI 4 (i.e. n = 4): DD|R
  Note: | denotes the boundary of sTTI n
To enable more DMRS sharing options in case of a RRC configured TTI length of 2os in UL, a DMRS-free UL sTTI, i.e. DD, can be indicated by an UL grant in sTTI#n-x which schedules sPUSCH in sTTI n, n  {1,2,4,5}, where x is processing time configured for a PUCCH group
sTTI 0
sTTI 1
sTTI 2
sTTI 3
sTTI 4
sTTI 5