## Slide 1: WF on UL power control
3GPP TSG RAN WG1 Meeting #89 R1-1709659
Hangzhou, P.R. China 15th – 19th May 2017
Agenda Item: 7.1.9
ZTE, Intel, Ericsson, InterDigital, Samsung, MediaTek, Nokia, ASB

## Slide 2: Background
  The following agreements for UL power control has been attached:
  For beam specific power control, NR defines beam specific open & closed loop parameters.
    FFS: details on beam common parameter(s)
    Note: Agreed on RAN1 #88 FFS details on “beam specific”, especially regarding handling layer/layer-group/panel specific/beam group specific/beam pair link specific power control
  gNB is aware of the power headroom differences for different waveforms, if the UE can be configured for both waveforms.
    FFS: offset configured/specified, reported,
    FFS on the details of power control parameters for example, P_c, Max or other open/closed loop parameter

## Slide 3: Proposal
  The following DL RS can be used for PL calculation for UL PC
    SSS of SS block;
    CSI-RS;
    FFS: DMRS for PDSCH/PDCCH;
    FFS: the applicable case for above DL RSs