## Slide 1: WF on CSI-RS for beam management
3GPP TSG RAN WG1 Meeting #89 R1-1709668
Hangzhou, China, 15th – 19th May, 2017
Agenda Item: 7.1.2.4.1
ZTE, LG Electronics, ASTRI, Huawei, HiSi, Samsung, Ericsson, InterDigital, CATT

## Slide 2: Proposal
  NR supports CSI-RS configuration to support Tx and/or Rx beam sweeping for beam management conveying at least the following information
    Information related to CSI-RS resource configuration
      E.g., CSI-RS RE pattern, number of CSI-RS antenna ports, CSI-RS periodicity (if applicable) etc.
    Information related to number of CSI-RS resources
    Information related to number of time-domain repetitions (if any) assoicated with each CSI-RS resource
      FFS: details of time-domain repetitions, e.g., signaling for time-domain repetitions may not be explicit
    FFS signaling details, e.g., explicit indication vs implicit indication
    Note this does not imply particular option (IFDMA or subcarrier scaling or DFT based) for sub time unit partition
    FFS: whether different sub-time units have same or different ports