## Slide 1: WF on additional evaluation assumption for V2X sTTI
CATT, CMCC, Huawei, Hisillicon, Nokia, ASB, OPPO, ZTE
3GPP TSG RAN WG1 Meeting #89 R1-1709744
Hangzhou, P.R. China, 15th – 19th May, 2017
Agenda item – 6.2.3.3.1

## Slide 2: Background
The following simulation assumptions and parameters was agreed for sTTI evaluation in meeting #88bis
Proportion of Rel-14 and Rel-15 UEs | (Rel-14 UE, Rel-15 UE) = {(50, 50)}. Other options not precluded. Two cases are evaluated for each proportion of UE combination; •case 1: Rel-15 UEs use 1ms TTI (SA and data) •case 2: Rel-15 UEs use short TTI (Companies to provide the detailed TTI structure)
Traffic model | Periodic broadcast traffic: Rel-14: 4 x 190 byte + 1 x 300 byte; 100 ms period; 100 ms latency Rel-15: 4 x 190 byte + 1 x 300 byte; 100 ms period; 20 ms latency Companies can bring results for other traffic models and latency.

## Slide 3: Background
There would be two phases for CoSdG:
- In Phase I, a baseline is proposed with a group of vehicles driving together with a lead vehicle are driven normally by a trained professional driver, and several following vehicles driven fully automatically by the system with information exchanged between the leader and other cars allowing with small distance (longitudinal gaps) between them. The typical required transmission frequency among the vehicles is up to 40Hz, [11], translating into 25ms end-to-end latency. Initial consideration of message exchange between vehicles in a platooning is based on CAM extension, which is around 300-400 bytes [11].
- In Phase II, all vehicles, the lead vehicle as well as following vehicles are driven fully automatically by the system. This will, compared to Phase I, allow smaller distance (longitudinal gaps) between them, leading to further reduction of fuel consumption. This requires in Phase II a higher transmission frequency compared to Phase I. The transmission frequency is 100Hz to coordinate the driving manoeuvre. The end-to-end latency is 1ms [13]

## Slide 4: Proposals
To include the additional mixed transmission scenario for V2X sTTI evaluation assumption
  Periodicity of 20ms for R15 and periodicity of 100ms for R14 in case of 140km/h
  Percentages of R14 and R15 UEs can be kept as agreed in #88bis or reported by companies
Traffic model | Periodic broadcast traffic: Mixed scenario 1(supported already in #88bis): Rel-14: 4 x 190 byte + 1 x 300 byte; 100 ms period; 100 ms latency Rel-15: 4 x 190 byte + 1 x 300 byte; 100 ms period; 20 ms latency Mixed scenario 2: Rel-14: 4 x 190 byte + 1 x 300 byte; 100 ms period; 100 ms latency Rel-15: 4 x 190 byte + 1 x 300 byte; 20 ms period; 20 ms latency Companies can bring results for other traffic models and latency.