## Slide 1: WF on SRS configuration
CATT, Ericsson, LG,
3GPP TSG RAN WG1 #89 R1-1709764
Hangzhou, China, May 15th – 19th 2017
Agenda Item: 7.1.2.4.4

## Slide 2: Proposal
For the purposes of DL/UL CSI acquisition and beam management
  A UE can be configured with K >= 1 SRS resources where
    A given X-port SRS resource spans N = 1,2, or 4 OFDM symbols within a slot where all X ports are mapped to each OFDM symbol of the resource
  A given SRS resource can be configured as aperiodic, periodic, or semi-persistent, where
    Periodic: The resource is configured with a slot-level periodicity and slot-offset
    Semi-persistent: The resource is configured with a slot-level periodicity and slot-offset
      Multiple SRS resources can be activated/deactivated with a single message
      FFS: Activation/deactivation details
    Aperiodic: The resource is configured without a slot-level periodicity and slot offset
      Multiple SRS resources can be triggered with a single message
    Note: For periodic/semi-persistent, different resources may have different periodicities and/or slot offsets
  FFS: Configuration details including grouping of SRS resources to allow low signaling overhead for indicating allocated SRS resources