## Slide 1: WF on Code Block Segmentation for BG #2
CATT, MediaTek, InterDigital, Ericsson…
R1-1714830
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, 21st – 25th August 2017
Agenda item 6.1.4.1.2

## Slide 2: Background (1)
RAN1 NR AH2 Agreement
  Base graph #1 is used for the initial transmission and subsequent re-transmissions of the same TB when
    CBS > X or code rate of the initial transmission > Y
  Base graph #2 is used for the initial transmission and subsequent re-transmissions of the same TB when
    CBS <= X and code rate of the initial transmission <= Y
  Working assumption : X = 2560 and Y = 0.67
  FFS after PCM decisions if X can be extended to 3840 and/or Y can be extended to 0.75

## Slide 3: Background (2a)
RAN1#88bis Agreements - The base graph design is selected from the following alternatives:
Alt 1: One base graph covering ~1/5 <= R <= ~8/9
Alt 1a: Two nested base graphs, where:
Base graph #1
  Covers info block size K:
Kmin1 <=K<= Kmax1, Kmin1 > Kmin, Kmax1 =Kmax
  Covers code rate R: ~1/3 <= R <= ~8/9; FFS whether Rmin can be ~1/5
Base graph #2
  Nested within base graph #1
  Covers info block size K:
Kmin2 <=K<= Kmax2, Kmin2 =Kmin, Kmax2 < Kmax, where 512<=Kmax2<=2560
  Covers code rate R: ~1/5 <= R <= ~2/3
  Kbmax =16 is the starting point; lower values in the range 10<=Kbmax<16 are encouraged if feasible.
  The set of supported shift sizes is taken from the set of shift sizes supported by the base graph supporting Kmax

## Slide 4: Background (2b)
Alt 2: Two base graphs, where:
Base graph #1
  Covers info block size K:
Kmin1 <=K<= Kmax1, Kmin1 > Kmin, Kmax1 =Kmax
  Covers code rate R: ~1/3 <= R <= ~8/9; FFS whether Rmin can be ~1/5
Base graph #2
  Not nested within base graph #1
  Covers info block size K:
Kmin2 <=K<= Kmax2, Kmin2 =Kmin, Kmax2 < Kmax, where 512<=Kmax2<=2560
  Covers code rate R: ~1/5 <= R <= ~2/3
  Kbmax = 10 is the starting point; higher values in the range 10<Kbmax<=16 can also be considered if necessary.
  The set of supported shift sizes is taken from the set of shift sizes supported by the base graph supporting Kmax

## Slide 5: Discussion
BG#1 is designed for code rate R: ~1/3 <= R <= ~8/9
BG#2 is designed for code rate R: ~1/5 <= R <= ~2/3
BG2 is optimized for code rate 1/5 <= R < 1/3

## Slide 6: Proposal
For code rate R < 1/3, the maximum code block size is: Kcb = 3840 and BG#2 is used
  For TB size larger than Kcb, the number of code blocks is determined by segmenting the code back based on maximum code block size Kcb = 3840